## Slide 1: Open Source Solution for Navigation System
Xun(Perry) Liu
4/10/2019

## Slide 2
05/2009
01/2010
03/2013
06/2014
Join Nav Team
Micro: Hybrid navigation solution supports Nav and Search
RMU, Tech Lead, simplify internal solutions
04/2018
OSRM
Valhalla
About myself
NGX, “Head of War Room”,
New infrastructure for Incremental update

## Slide 3
Story 1: How Valhalla organize map data for map streaming
Story 2: How OSRM calculate route with dynamic information
Story 3: How Lyft do map matching when map data is wrong
Agenda

## Slide 4
Terminology
Node
Edge
Graph
Shortest Path
Start
End
Tile2
Tile1

## Slide 5
Story 1: How Valhalla organize map data for map streaming
- Background
- Ngx’s solution
- Valhalla’s solution
Story 2: How OSRM calculate route with dynamic information
Story 3: How Lyft do map matching when map data is wrong
Agenda

## Slide 6
Story #1. How Valhalla organize mapdata for map streaming
Streaming for offline navigation

## Slide 7
How to store data
Problem to solve: How to find nearest charge station for your EV?
Notes: Assume all rider is just at static location
Group elements near each other together
Group size should be balanced

## Slide 8
Story 1: How Valhalla organize map data for map streaming
- Background
- Ngx’s solution
- Valhalla’s solution
Story 2: How OSRM calculate route with dynamic information
Story 3: How Lyft do map matching when map data is wrong
Agenda

## Slide 9: NGX Solution - Divide based on content
Tiles size are balanced(average file size is 700KB)
Element might move to different tile during data update
Notes: Add current data statistics

## Slide 10
Story 1: How Valhalla organize map data for map streaming
- Background
- Ngx’s solution
- Valhalla’s solution
Story 2: How OSRM calculate route with dynamic information
Story 3: Map Lyft do map matching when map data is wrong
Agenda

## Slide 11: Valhalla’s Solution - Divide based on map
Fixed boundary split
Element will stay in fixed grid as long as no change for geometry
Tile id could be calculated by lat/lon
Cacheability/Updateability
File size depend on data density
25MB

## Slide 12
Valhalla Tiles

## Slide 13
Valhalla Streaming
Notes: What is Valhalla

## Slide 14
Lesson learned from Valhalla
Improvement on Current product
Fix boundary at space level, then try at tile level
Fixed size tiles make streaming easier, but have impact on performance and memory

## Slide 15
Story 1: How Valhalla organize map data for map streaming
Story 2: How OSRM calculate route with dynamic information
- Background
- Ngx’s solution(FC promotion)
- OSRM’s solution(CRP)
Story 3: Map Lyft do map matching when map data is wrong
Agenda

## Slide 16
Story #2 Calculate route consider dynamic information

## Slide 17: Story #2 Calculate route consider dynamic information
Chanllege of routing + dynamic information
40M edges for HERE NA
80M edges for HERE EU
Notes: Dikjstra

## Slide 18: Story #2 Calculate route consider dynamic information
Chanllege of routing + dynamic information
Notes: Dikjstra

## Slide 19
Story 1: How Valhalla organize map data for map streaming
Story 2: How OSRM calculate route with dynamic information
- Background
- Ngx’s solution(FC promotion)
- OSRM’s solution(CRP)
Story 3: Map Lyft do map matching when map data is wrong
Agenda

## Slide 20
NGX Solution - Function class Level promotion

## Slide 21
NGX Solution - Function class Level promotion

## Slide 22: Function class Level promotion
Prune and Shrink
When to promote
Notes: What is candidate

## Slide 23
Function class Level promotion
Miss best candidate
Only promote, never look down

## Slide 24
Story 1: How Valhalla organize map data for map streaming
Story 2: How OSRM calculate route with dynamic information
- Background
- Ngx’s solution(FC promotion)
- OSRM’s solution(CRP)
Story 3: How Lyft do map matching when map data is wrong
Agenda

## Slide 25
How to calculate route
Notes: Picture layout

## Slide 26
Thomas Guide
Notes: Picture layout

## Slide 27
Partition the graph
Access Points
Access Points
Access Points
Keep update cost between access points

## Slide 28: Customizable Route planning
Step 1: Graph preprocessing
Graph partition, preprocessing, hours
Step 2: Customization
Apply dynamic information with cost model
Each round of traffic update, seconds
Step 3: Query
Real time, per request, mili-seconds

## Slide 29
What’s the balanced-minimum cut

## Slide 30: Max Flow Min Cut

## Slide 31
Try different cut to find minimum

## Slide 32
Partition graph of US

## Slide 33
Lesson learned from OSRM
Container/Dynamic Configuration/Cucumber
Routing as service
Improvement on Current product
Cloud side use different strategy with embedded side
Accurate algorithm matters especially for ML

## Slide 34
Story 1: How Valhalla organize map data for map streaming
Story 2: How OSRM calculate route with dynamic information
Story 3: How Lyft do map matching when map data is wrong
Agenda

## Slide 35: Story #3 Map Matching when the map data is wrong
A story about Lyft pick up
No Map data
When Map data exists
Notes: The original picture tells the feature of destination adjustment from Lyft

## Slide 36
Offline Map Matching
What/How/Why
Give a sequence of GPS signals, find the most probable sequence of road segments
Notes: What is gps point

## Slide 37: Offline Map Matching
What/How/Why
Historic/Live traffic/ETA
Enhance map data
User pattern
Notes: Live traffic
Enhance map data
Analysis user pattern

## Slide 38: Offline Map Matching
What/How/Why
Noise & Sparseness
Missing GPS
Wrong/Complex Map Data
Notes: ['tʌnl]

## Slide 39: Offboard Map Matching logic
How
Filter noise points
Find Nearest edges as Candidate
Consider Connectivity
Optimal path
99% (2.05*errsize)
95% (1.65*errsize)
67% (1.00*errsize)
DR Fix
Road Width
dmin
MM Fix
Hidden Markov Map Matching
Emission Probability
Transition Probability
Viterbi Algorithm
Kalman Filter

## Slide 40
When map is wrong
High confidence
High confidence
Low confidence

## Slide 41
Lesson learned
Application is not the key of success, the data is.

## Slide 42: When map is wrong (LYFT’s way)